To do :
1/(1+abs(x))

Gaussian_like_activation
This is a simplified Gaussian function.
This layer is designed as an activation function to replace the real Gaussian function. It’s probably easier to understand and light weighted for computer to calculate. It works basically the same way as real Gaussian function, but it doesn’t guarantee the integral to be 1 at all.

Formula:
result = (x^(2*l))/sigma
This works only when l is some specific numbers. Sigma must be greater than 0.
Though I may mess with the mass :)
Since it doesn’t meet the need of automatic adjustment. So, in practice, I used:
result = ((x*x)^l_like) / (sigma_like* sigma_like)
to make sure it’s an even function, and also the denominator is greater than or equals to 0. When it equals to zero, the forward function modifies it to some small number(epi in code)before it does any real tasks.

Gaussian_like_activation_Parabola_Leaky_ReLU
[[[ !!! This is not recommended by me !!! ]]]
Since Gaussian looks like a bell and works super great, I guess anything looks like a bell would also work. The formula is
result = Leaky_ReLU(1-a*x*x)
Basically it’s a parabola( ax2+bx+c ). In this case, a<0, b == 0, c == 1.
I didn’t protect the parameter of a not to be 0. The issue for this activation is not here.
According to my test, the output of this layer doesn’t hold around 1. It goes down to 0 too fast. The Gaussian function(both real version and my simplified version) has a plain structure where output value holds around 1.
I didn’t test this layer in real image, but it doesn’t work well enough in a simple test case:

   Ground truth

   1 torch.nn.Linear layer with 16 units. And then this Gaussian_like_activation_Parabola_Leaky_ReLU.

   2 torch.nn.Linear layer with 16 units. And then this Gaussian_like_activation_Parabola_Leaky_ReLU.
As the results show, the activated area is very blur.